Specification for laptop battery tester RFNT2

Summary	2

Basic Parameters	2

Function Introduction	3

Charge	3

Test	3

Online Functions	3

Monitoring	3

Control	4

Parameters	4

Others	4

Structure	5

Accessories	5

Front Pannel	5

Back Panel	6

Top Panel	6

Bottom Panel	6

Display Mode	7

LCD Display	7

LED Indication	7

Operation	8

Power Up	8

Connecting Battery	8

Charge	8

Test	8

Online Functions	9

Cautions	9

# Summary

RFNT2 is a battery testing device with two channels, having the features below:

- Supporting two intelligent batteries at once:

- With charge and test functions

- LCD for displaying battery information

- LED for indicating working status

- Pre-charge, fast charge and constant voltage charge for charging stages

- With a USB port for connecting with computers, master machine can monitoring and control slave machine

# Basic Parameters

Dimensions: 201 x 99 x 35 mm

Weight: 333g

Adapter   Input: AC 100 ~ 240 V   Output: DC 19V 4.74A

Display mode

Segment LCD with white backlight + LED in red and green

Charging mode

Constant current + constant voltage

Charging current

Maximum charging current of each channel: 2.5A

Standby power consumption≤1W

Working temperature

0~40℃        20%－90% RH (Non condensation)

Storage temperature

-20℃~65℃    10%－95% RH (Non condensation)

Maximum charging time: 8 hours

# Function Introduction

## Charge

Two channels can work independently and serve two intelligent batteries separately. Active, pre-charge, constant current and constant voltage are the stages of charging mode. The initial charging mode depends on the battery voltage, so active and pre-charge don't happen to every batteries.

## Test

Testing time is 30seconds and the purpose is to check both the charging and discharging performances. After finishing test, LED flickers with green color and LCD reports the test result.

Normal:              Test           OK            Shown on LCD

Abnormal:            Test           NG            Shown on LCD

Possible causes and solutions for the abnormal:

- Cause: battery voltage is too low to discharge

Solution: try to charge the battery to raise voltage

- Cause: remaining capacity is too full to charge any more

Solution: try to discharge the battery to reduce the remaining capacity

- Bad contact of battery connecting wires

- Damaged battery

- Tester trouble

## Online Functions

Tester can be connected with master machine via a USB port. Users can monitor, control and set parameters via Battery Manager software in the master machine.

## Monitoring

Battery information can be monitored via three windows.

- Home screen

Battery bar and brief information can be read on home screen.

- Battery detail information window

Show smart battery data in real time and the data can be saved and printed in image format.

- Battery graph window

Voltage, current and capacity are traced in curves.

## Control

Battery Manager can control slave machine completely. Right-click menu on the battery bar includes the related commands.

## Parameters

Users can set working parameters via set parameter window in Battery Manager.

## Others

- Active cooling

- Active batteries of zero voltage

When a battery is deep discharged, the discharge protection circuit will start up and the voltage in the battery connector will become zero voltage. In this case, an appropriate voltage should be supplied to active the battery.

- Battery identification

Battery information can be read from battery management chip after establishing communication.

- Intelligent protection

Against over-current, over-voltage, over-charge, over-heat and short circuit.

- Suitable for almost all laptop batteries, above 95%

# Structure

## Accessories

1).1 x adapter

2). 1 x USB cord

3). 1 x CD

4). 13 x connectors

5). 10 x cables

6). 10 x jumpers

## Front Panel

①Segment LCD

②LED for A channel

③LED for B channel

④Backlight switch button

⑤Test button

⑥Charge button

⑦Channel switch button for checking battery information showed on LCD screen

## Back Panel

- Heat dissipation holes

## Top Panel

- AC input jack

- Heat dissipation holes

- mini USB port

## Bottom Panel

- Connecting wire jack for connecting to the battery of A channel

- Heat dissipation holes

- Connecting wire jack for connecting to the battery of B channel

# Display Mode

## LCD Display

- Battery voltage

- Remaining capacity

- Charging current or discharging current

- Remaining capacity percentage

- Charge / discharge cycle count

- Full charge capacity

- Test result

- Channel indication

- Battery bar

## LED Indication

Shine in red color:  On charge or discharge

Flicker in red color:  Trouble alarm

Shine in green color:  Charge finished

# Operation

## Power Up

- Connect the adapter to AC power source

- Connect the tester with the adapter

LCD shows battery information and LED lights up for a moment if a battery has been connected to the tester.

Both LCD backlight and LED lights up for a moment if no battery has been connected to the tester.

## Connecting Battery

1). Make sure the connecting wire fits the battery

2). Make sure the connecting wire is plugged into the battery socket in correct direction

3). Make sure no poor connections

## Charge

1). Normal charge

Tester starts to charge your battery after you press the charge button. Battery information will be showed on LCD screen in real time.

2). Active charge

If the battery needs to be activated, tester can not show any battery information. In this case, you should press the charge button to start up active charge. Tester will go into normal charge process after the battery is activated successfully.

Time limit of active charge: 60 seconds

## Test

Tester starts to test your battery after you press the test button. Charging / discharging current and test result will be showed on LCD screen.

## Online Functions

- Connect tester to your computer via USB cord

- Startup Battery Manager

- Refer to Battery Manager User Manual

Remarks: Battery Manager software and USB drive program should be installed in your computer before you use this function.

# Cautions

- Use the fitted adapter. Nonstandard adapters might lead to working disability.

- To avoid explosion and danger, damaged batteries and leaking batteries are not allowed.

- The product is good for indoors. Do not expose and use it in outdoors.

- Do not drop or put something heavy on it.

- Children are not allowed to use the product without adults.

- Do not keep the product under the direct rays, beside the hot devices or in other hot environment.

- Do not disassemble or assemble the product